## Slide 1: Multi-parameter Signal Analysis for Patient Monitoring
ECE 313 – Section G
Mini Project 2

## Slide 2: Multi-parameter Signal Analysis for Patient Monitoring
In this Project, you will do:
  Analyze data by calculating/plotting the empirical distributions using physiological monitoring data
  Compare an empirical distribution with an estimated normal distribution from estimated parameters (μ, σ)
  Determine a threshold to find abnormalities of each monitored signal
  Generate alarms for each signal
  Implement a voter that makes the final decision
  Perform an 3-fold cross validation
and you will learn:
  to calculate the pmf/pdf and cdf based on empirical data
  the characteristics of pmf and pdf
  the relationship between pmf, pdf, and cdf
  properties of the Normal distribution
  to evaluate the performance of a monitoring system which has false alarms and missed detections

## Slide 3: Multi-parameter Signal Analysis for Patient Monitoring
Assume you are an engineer working at a medical device company ACME
You are assigned to design a reliable patient monitoring system which analyzes the correlated physiological signals collected from the patient’s body, and generates alarms for abnormalities.
You are given a set of three correlated physiological signals collected from the biomedical sensors attached to the patient’s body:
  S1: Heart Rate (HR)
  S2: Pulse Rate (PR)
  S3: Respiration Rate (RESP)

## Slide 4: Mini Project 2: Description
You design a multi-parameter and fusion monitoring system where
The signals are passed through three processing units (P1, P2, and P3, respectively), called threshold functions, to detect patient abnormalities.
Each threshold function will generate an alarm whenever a data sample of the corresponding signal exceeds a pre-defined threshold. A “1” on the output of each function indicates an alarm and a “0” corresponds to absence of an alarm.
A majority voter function then generates the final output, based on the value that the majority of the threshold functions agreed upon.
Figure 1

## Slide 5: Majority Voter Example
Heart Rate Alarms
Pulse Rate Alarms
Respiration Rate Alarms
Figure 2
Notes: Blood pressure and heart rate signals are monitored using a mean analysis technique where during the training period the mean and standard deviation of samples are calculated and is used in the monitoring phase as a patient-specific signature for detection of abnormalities.

## Slide 6: Voter Success Examples
Assume that by talking to the physician, we know that in the time interval T the patient experiences an abnormality and an alarm should be raised (The output from the monitoring system should be “1”).
If P1 and P2 functions generate “1”, but P3 generates a “0”, then the majority voter will generate a “1” (an alarm) on the final output, indicating a patient abnormality.
  This means that P3 missed a true alarm, and voter fixed a missed detection on P3.
Assume that for another time interval we know the patient experienced no abnormality and no alarms should be raised (The output should be “0”).
If P1 generates a “1”, P2 and P3 functions generate “0”, then the majority voter will generate a “0” (no alarm) on the final output, indicating no patient abnormality.
  This means that P1 raised a false alarm, and the voter masked a false alarm on P1.

## Slide 7: Voter Failure Examples
Again, assume that by talking to the physician, we know that in the time interval T the patient experienced an abnormality and an alarm should be raised (The output from the monitoring system should be “1”).
But both P1 and P2 functions generate “0”, while P3 generates a “1”, then the majority voter will generate a “0” (no alarm) on the final output, wrongly indicating that there is no patient abnormality.
  This means that P3 raised a true alarm, but because P1 and P2 had missed detection, the voter output was erroneous. We call this a missed detection.
Now assume that for another time interval we know the patient experienced no abnormality and no alarms should be raised (The output should be “0”).
If P1 generates a “0”, but P2 and P3 functions generate “1”, then the majority voter will generate a “1” (an alarm) on the final output, indicating a patient abnormality.
  This means that P1 raise a true alarm, P2 and P3 raised false alarms, and the voter output was erroneous. We call this a a false alarm.

## Slide 8: Task 0: Data Import & Preparation
Task 0:
  You are provided with a dataset patient_data.mat, a main skeleton code, and two skeleton codes for functions pdf_cdf and threshold_func.
patient_data consists of 2 variables:
  data (physiological signals) and golden_alarms (physician annotations)
data is an array of 3 rows and 30,000 columns
  The first row corresponds to the Heart Rate (HR), the second row corresponds to the Pulse Rate(PR), and the third row corresponds to the Respiration Rate (RESP)
  Each column corresponds to a data sample (there are 30,000 data entries for each signal)
  Sampling rate is 1 sample/second and the whole period is 30,000 seconds.
golden_alarms is a single row of 3,000 columns, each entry is a binary value
  Each entry corresponds to an interval containing 10 samples.
  Any of the samples contain an alarm in a given interval, the entry is 1 if it contains alarms, 0 if there are no alarms.
Run the following parts provided in the skeleton code:
Load the provided data set into MATLAB: load patient_data.mat
In order to visualize the data, as in Figure 2, plot all three signals over time.

## Slide 9: Task 1.1: Data Analytics
  For the Respiration Rate (RESP) signal:
The skeleton code generates three different sample sets of sizes 70, 1000, 30,000 sample points from each signal. You should now write function pdf_cdf to plot: i) the pmf using the discrete samples, ii) estimated pdf using the continuous data, and iii) the cdf. For each sample set X:
    Find the pmf of Y = floor(X), i.e., the distribution of sample points in different intervals of data (e.g. what is the percentage of samples in interval 3 ≤ RESP < 4). Hint: Use unique(floor(X)) to get the list of intervals and hist function to get the frequencies (Remember that 0 ≤ P(X) ≤ 1). Plot the pmf using bar function.
    Plot the estimated pdf* for the signal using the code provided to you in the skeleton. What differences do you see between the pmf plotted in part 1 above and the estimated pdf?
    Use the ecdf function in Matlab to calculate and plot the CDF in the same figure.
    Hint: The CDF of the whole data set (k = 30,000) is plotted for you as a reference point to compare with. Use hold on to plot all the graphs in the same figure.
What differences do you see as the sample sizes increase from 70 to 30000?
Notes: Note that hist returns counts, but we should derive probabilities

## Slide 10: Task 1.1 (Cont.)
  For the Respiration Rate (RESP) signal:
Use the tabulate function in MATLAB over X (sample size k = 30000) and Y(=floor(X)). tabulate(X) will give you the value of pdf for each sample point, while tabulate(Y) will give you a pmf. Find the minimum and maximum probability values found by the tabulate function in each case.
Explain why tabulate(X) gives a pdf while the other gives a pmf.
What difference do you find for the derived min, max for each distribution
Can you relate the difference to identify a distinct characteristics of a pdf?
(Hint: see class lecture notes
Related to part a.2: See the following links for more information on kernel density estimation based on data:
http://en.wikipedia.org/wiki/Kernel_density_estimation
http://www.mathworks.com/help/stats/kernel-distribution.html
Notes: Note that hist returns counts, but we should derive probabilities

## Slide 11: Task 1.1 (Cont.)
  (TRAINing) In order to design an efficient threshold function, you need to find an interval of X where 96% of probability for signal lies. Assume that an anomaly happens when the data sample falls outside of this range on any of the two tails of distribution.
  You will determine the thresholds in two ways, using the data (Task 1.1.c) and assuming a normal distribution (Task 1.2)
  These thresholds are subsequently used in task2.1.a to generate alarms from the given signals.
  Based on the CDF of the signal (sample size k = 30,000) that you calculated in part a, find values a and b such that P(X ≤ a) ≤ 0.02 and P(X ≤ b) ≥ 0.98.
Figure 3
Notes: Note that hist returns counts, but we should derive probabilities

## Slide 12: Task 1.2: Data Analytics
  For the Respiration Rate (RESP) signal:
  Calculate the mean and standard deviation of the signal over the whole period for the 30,000 samples
    Hint: You can use mean and std functions in MATLAB
  Use the normrnd function in MATLAB to generate a normally distributed random variable with the mean and standard deviation that you found for the signal in part (a) and plot the pdf and CDF of this normal random variable.
  Use the normplot function in MATLAB to estimate the difference between the distribution in Task 1.1 and the corresponding normal distribution here.
  What differences do you see between the distribution generated in this task and the plot from Task 1.1 for 30K sample size?
  Hint: See http://en.wikipedia.org/wiki/Skewness
  d) Write the equation for pdf and CDF of the normal distribution that you generated in part b. Use the normal distribution table (described in Lectures 11-12) to find values a and b such that P(X ≤ a) ≤ 0.02 and P(X ≤ b) ≥ 0.98.
  What differences do you see compared to the values of a and b in Task 1.1?

## Slide 13: Task 2.1:Anomaly Detector
  (TESTing)
  Use the empirical thresholds (a and b) shown in Table 1 (Slide 15) and call the provided threshold functions to generate alarms for each of the HR, PR, and RESP variables. Remember that a “1” on the output from each threshold function indicates an alarm and “0” corresponds to absence of an alarm.
  Coalescing of alarms: The alarms generated for each of the variables HR, PR, and RESP are then coalesced separately over fixed intervals of 10 samples. For example, if for HR there is at least one alarm generated during an interval of 10 samples, then the output for that interval will be “1”, similarly for PR, and RESP.
  Write a majority voter function that takes as input each of the 10-sample windows and votes on the alarms generated from each threshold function in part (b). The output of the voter will then a sequence of alarms that the majority (at least 2 out of 3) of the functions agreed on.
  Use the bar function in MATLAB to plot the coalesced alarms generated for each variable (in part b) and the final alarms generated by the majority voter (in part c). (Hint: Each bar will represent an alarm (“1”) during a 10-sample window).

## Slide 14: Task 2.2: Detector Evaluation
  You are given by the physician a vector of golden alarms (golden_alarms variable) which indicates for each 10-sample interval whether patient was diagnosed an actual abnormality (“1”) or not (“0”).
  - A false alarm corresponds to the case where an alarm (“1”) is generated based on processed input data for an interval, but no abnormalities (“0” in the golden alarms) are detected by the doctor for the same input data.
  A miss detection corresponds to the case where no alarm (“0”) is generated based on processed input data for an interval, but at least one abnormality (“1” in the golden alarms) is detected by the doctor for the same input data.
  Calculate the probabilities of false alarms and miss-detections for the whole system (Show all your work).
      Recall that the voter operates on coalesced alarms, generated in part (b).
      P(False Alarm) = P(Voter raises an alarm | Physician indicates no abnormality)
      P(Miss Detection) = P(Voter raises no alarms | Physician indicates an abnormality)
  Calculate the probability of error.
    P(Error) = P(Voter raises an alarm AND Physician indicates no abnormality)+
    P(Voter raises no alarm AND Physician indicates an abnormality)

## Slide 15: Task 2.2 (Cont.)
c) Perform Tasks 2.1 and 2.2 again, this time with the theoretical thresholds (a and b) found in Task 1.2 - part d and Table 1. What differences did you see in the probabilities of miss-detection, false-alarm, and error for each signal?
What lessons did you learn by observing the results generated by the empirical approach vs. the theoretical approach?
Provide your explanations in at least three bullets.
Table1
Signal | Empirical Thresholds | Theoretical Thresholds
Heart Rate (HR) | a = 80.17, b = 98.52 | a = 78.84, b = 96.83
Pressure Rate (PR) | a = 79.00, b = 97.07 | a = 78.15, b = 96.09
Respiration Rate (RR) | To be calculated in Tasks 1.1.a and 1.1.b | 

## Slide 16: Task 3: 3-fold Validation
In Task 1 and Task 2, we have designed a decision logic (TRAINing) and evaluated (TESTing) it on the same dataset. However, the testing data might not always be available at the point of training. Here we introduce you 3-fold validation for a more realistic evaluation.
Divide the data into three subsets of equal length. Hint! d1 = data[:, 1:100000]; can be used for parsing the first 1/3 of the data Divide the golden_alarms into three subsets of equal length. Caution! Note that the length of golden_alarms is not the same as data
For each subset: TRAIN the decision model using the remaining subsets and using the detector from the TRAIN step, TEST it on the subset (store the performance) e.g., let d1, d2, d3 be the three subsets. Keep d1 for TESTing. Perform data analytics on d1+d3 and find the thresholds a, b(TRAIN). Using a, b and d1, TEST the performance of the detector implemented in Task 2. Same procedure repeated with d2, and d3 for testing Hint! train_data = [d1 d3]; can be used for combining the two subsets
After repeating (b) over each of the three subsets, average the three sets of performances saved from the TEST procedures. How do the averages (of P(false alarm), P(miss detection), P(error)) compare to the results from Task 2.2?
(Optional) Reading for your own interest:
n-fold cross validation
Overfitting

## Slide 17: Project Timeline and Grading
Tasks 0-1: due on Friday, March 3rd, 11:59 PM.
  Submit your answers for Task 1 and a working MATAB script
All Tasks: due on Friday, Mar 10th, 11:59 PM.
  Submit your report and a working MATLAB script
Grading
  Task 1: 40%
  Task 2: 30%
  Task 3: 30%
Checkout the class website for description of the project, tasks, and data set, as well as your group assignments: http://courses.engr.illinois.edu/ece313/SectionG/projects.html
Contact your group members to start the project as soon as possible.

## Slide 18: Project Submission
A report describing your work and results and your Matlab code must be delivered electronically to the TA by the due date: Submissions will be done through Compass
Matlab code Instructions:
  We provide you with a skeleton file to start from.
  Fill in the code related to each task in the sections indicated by comments.
  fprintf() functions are provided for structured results. Please replace the variables accordingly to report your results.
  TAs will execute your code & check the results. Non-executable code will not be graded.
Report Instructions (follow all steps):
  Format your report to separate different tasks in separate sections.
  Copy results generated by fprintf() functions into corresponding sections in report.
  Explain all your work and assumptions made for deriving your results.
  Incorrect final answers without any explanations or comments receive zero credit.
  Non-readable reports will be returned without a grade.
  Include your names, group name. Each group member must affirm that she/he has worked on the project and has read and agrees with the final report

## Slide 19: MATLAB Tutorial
Files:
  Function and codes: .m
  Files: .mat
Import a data set into MATLAB workspace:
  load patient_data.mat
Export a data set from the MATLAB workspace:
  save result.mat
  save result.mat X, Y, Z
Clear all the workspace environment:
  clear all
Clear the command window:
  clc
You can repeat the previous commands by arrow keys or from the command history window

## Slide 20: MATLAB Tutorial (Cont.)
Define variables in the command window:
  x = 1
  y = X + Z
  z = cos(1)
To define arrays:
  T = [1, 2, 3, 4, 5]
  T = 1:5
  W = [1, 1.1, 1.2, 1.3, 1.4, 1.5]
  W = 1:0.1:1.5
  Labels = {‘Heart Rate’, ‘Blood Pressure’, ‘Electrocardiogram’}
  T = [1, 2, 3; 4, 5, 6] (An array of 2 rows and 3 columns)
To see the values of variables, just type their name:
  x
  W(1)
  T(2:3)

## Slide 21: MATLAB Tutorial (Cont.)
Define a vector of zeros or ones:
  zeros(1,10) (A vector of 10 columns, all initialized to 0)
  ones(2,3) (An array of 2 rows and 3 columns, all initialized to 1)
Find the size of a vector or array:
  size(T)
  size(W, 2)
Plotting a variable
  plot(x)
  plot(t, x)

## Slide 22: MATLAB Resources
MATLAB Tutorials and Learning Resources:
  http://www.mathworks.com/academia/student_center/tutorials/launchpad.html
    Watch short videos and look at MATLAB examples.
    Read the user’s guide.
  MATLAB help:
    help hist
    doc hist